## Slide 1: Android Network Sniffer
Group SS18/2A
Team Members:
Soh Yu Xuan 5498636
Timothy Chin 5498399
Kenneth Huang 5498442
Kendrick Tan 5026556

## Slide 2: Introduction
A network sniffer is a tool that monitors or sniffs out the data flowing over computer network links in real time.
Network Sniffers can take a snapshot copy of the data without redirecting or altering it.
Without the proper configurations, a Network Interface Card (NIC) card in a normal mode will generally ignore all comings and goings of traffic for other devices

## Slide 3: Types of Modes
There are two options in which a Network Interface Card (NIC)
Promiscuous Mode
  A Mode in which the NIC card is connected to a network and enables the NIC to see all packets being routed in the network
Monitor Mode
  A mode in which the NIC does not need to be connected to a network that enables the NIC to see all packets in the vicinity

## Slide 4: What are packets?
A packet is the unit of data that is routed between an origin and a destination, on the internet or any other packet-switched network.

## Slide 5: Android v. Linux architecture
Android’s kernel is derived from Linux, not the same but very similar
Android permissions are far different from Linux (configurability wise) as more emphasis is given for ease of use. (Why would normal users want a shell for their Android device?)
Termux is a command line interface application and is used as we test and develop NetSniffer

## Slide 6: Android Hardware Requirements
Most PCs have NIC cards that can be set to promiscuous or monitor mode without much hassle.
On Android devices however, it may range from difficult, to impossible. Manufacturers do not support fiddling with hardware, with only enthusiasts working on related projects at their own risk.
NIC cards require drivers to update their firmware to allow monitor / promiscuous mode. On PC it is easy and can be done in a few clicks. On Android, the Linux kernel has to be extracted via binary dump, have the drivers installed in the correct locations, and recompile the entire OS, then the device has to be re-flashed with the new OS.

## Slide 7: What are binaries? Why use binaries?
Binary executables are compiled with their required libraries and can be executed without any other interpretation or file.
Binaries for NetSniffer have to be compiled with their required libraries for the ARM architecture (for Android).
Instead of binaries, executables can be written into an apk file itself. Libraries such as Libpcap and Jnetpcap can be integrated with the application, however, it is impossible to grant an application root user privileges
Therefore, binaries have to be used, then executed within the application

## Slide 8: TCPDump & Libpcap
TCPDump is a free software designed by Van Jacobson, Sally Floyd Vern Paxson and Steven McCanne in 1988. It is built with libpcap library in C to read packets from a network interface card.
wget http://www.tcpdump.org/release/libpcap-1.8.1.tar.gz
tar -xf libpcap-1.8.1.tar.gz
sudo apt-get update
sudo apt-get install flex
sudo apt-get install bison
cd libpcap-1.8.1
./configure –prefix=/usr
make
sudo make install

## Slide 9: Rooting an Android device
Rooting of an Android device is how a user gets complete access to everything in the OS, which adds the command “su” or superuser to Android
On Android, enthusiasts would find ways to escalate their privileges to superuser, which is NOT supported by their manufacturers and results in voiding of warranty
As such, rooting of devices differ and there is no surefire or standard way to root a device, and attempts to root a device may result in a “bricked” device, breaking the device.
We have attempted multiple attempts to root our chosen device, the Nexus 5 with several solutions, but finally achieved root with “CF-Auto-Root”
Permissions are managed with the external application SuperSU

## Slide 10: Difficulties faced
HW has to be compatible (NIC)
  Only specific devices can be used
Root privileges
  Unable to debug / test on emulator
  Unsupported and experimental
  Process has to be used, and managed, not much support available

## Slide 11: Diagrams - Class

## Slide 12: Diagrams - Use Case

## Slide 13: Diagrams - Sequence

## Slide 14: Sequence Sniff Start Mon

## Slide 15: Sequence Sniff Start Prom

## Slide 16: Sequence Start Mon

## Slide 17: Sequence Start Prom

## Slide 18: Sequence Stop Capture

## Slide 19: Sequence Help

## Slide 20: Sequence Map Feature

## Slide 21: Sequence Map Start

## Slide 22: Sequence Map Stop

## Slide 23: Sequence Start Map Network

## Slide 24: Sequence Start OS Map Network

## Slide 25: Sequence Check Resource

## Slide 26: Diagrams - Activity Sniff

## Slide 27: Diagrams - Activity Map

## Slide 28: Diagram - Activity AnalyzePCAP

## Slide 29: AGILE
We decided AGILE development was the most appropriate.
AGILE software development describes an approach to software development in which the requirements and solutions continually evolve.
AGILE is most appropriate as these variations of software were not prevalent in Android, with mostly experimental support
Our solutions change often with heavy emphasis on prototyping and continual programming to find solutions that satisfy our stipulated functionalities

## Slide 30: VCS & Documentation
The version control we chose was GitHub